## Slide 1: CS427 Multicore Architecture and Parallel Computing
Lecture 3 Multicore Systems
Li Jiang
2014/9/24

## Slide 2: An Abstraction of Multicore System
How is parallelism managed?
Where is the memory physically located?
How the processors work?
What is the connectivity of the network?

## Slide 3: Flynn’s Taxonomy
classic von Neumann
not covered

## Slide 4: MIMD Subdivision
SPMD
  Single Program Multiple Data: Multiple autonomous processors simultaneously executing the same program (but at independent points, rather than in the lockstep that SIMD imposes) on different data.
MPMD
  Multiple Program Multiple Data: Multiple autonomous processors simultaneously operating at least 2 independent programs. The "host" runs one program that farms out data to all the other nodes which all run a second program.

## Slide 5: Two Major Classes
Shared memory multiprocessor architectures
  A collection of autonomous processors connected to a memory system.
  Supports a global address space where each processor can access each memory location.
Distributed memory architectures
  A collection of autonomous systems connected by an interconnect.
  Each system has its own distinct address space, and processors must explicitly communicate to share data.
  Clusters of PCs connected by commodity interconnect is the most common example.

## Slide 6: Shared Memory System

## Slide 7: UMA Multicore System
Uniform Memory Access: Time to access all the memory locations will be the same for all the cores.

## Slide 8: NUMA Multicore System
Non-Uniform Memory Access: A memory location a core is directly connected to can be accessed faster than a memory location that must be accessed through another chip.

## Slide 9: Programming Abstraction
A shared-memory program is a collection of threads of control.
Each thread has private variables, e.g., local stack variables
Also a set of shared variables, e.g., static variables, shared
common blocks, or global heap.
Threads communicate implicitly by writing and reading shared variables.
Threads coordinate through locks and barriers implemented using shared variables.

## Slide 10: Case Study
256KB L2
Unified Cache
32KB L1
Instr Cache
32KB L1
Data Cache
Shared 8MB L3 Cache
Up to 16 GB Main Memory (DDR3 Interface)
Proc
256KB L2
Unified Cache
32KB L1
Instr Cache
32KB L1
Data Cache
Proc
256KB L2
Unified Cache
32KB L1
Instr Cache
32KB L1
Data Cache
Proc
256KB L2
Unified Cache
32KB L1
Instr Cache
32KB L1
Data Cache
Proc
Bus (Interconnect)
Intel i7-860 Nehalem
Support for SSE 4.2 SIMD instruction set
8-way hyperthreading (executes two threads per core)
Multiscalar execution (4-way issue per thread)

## Slide 11: Case Study
Sun UltraSparc T2 Niagara
FPU
Support for VIS 2.0 SIMD instruction set
64-way multithreading (8-way per processor, 8 processors)
Proc
FPU
Proc
FPU
Proc
FPU
Proc
FPU
Proc
FPU
Proc
FPU
Proc
FPU
Proc
FPU
Memory
Controller
512KB
L2
C$
512KB
L2
C$
Memory
Controller
512KB
L2
C$
1
52KB
L2
C$
Memory
Controller
512KB
L2
C$
512KB
L2
C$
Memory
Controller
512KB
L2
C$
512KB
L2
C$
Full Cross-Bar (Interconnect)

## Slide 12: Case Study
Nvidia Fermi GPU

## Slide 13: Case Study
Apple A5X SoC
2 ARM cores
4 GPU cores
2 GPU Primitive Engines
Other SoC components: WIFI, Video, Audio, DDR controller, etc.

## Slide 14: Distributed Memory System

## Slide 15: Programming Abstraction
Distributed-memory program consists of named processes.
• Process is a thread of control plus local address space -- NO shared data.
• Logically shared data is partitioned over local processes.
• Processes communicate by explicit send/receive pairs
• Coordination is implicit in every communication event.

## Slide 16: Case Study
Year

## Slide 17: Case Study
Jaguar
Oak Ridge National Laboratories
Cray XT5 supercomputer
2.33 Petaflops Peak
1.76 Petaflops Sustain
224256 AMD Opteron cores
3-dimensional toroidal mesh

## Slide 18: Case Study
Tianhe (TH-1A)
Chinese National University of Defense Technology
4.7 Petaflops Peak
2.5 Petaflops Sustain
14336 Intel X5760 (6-core) CPUs
7168 Nvidia M2050 Fermi GPUs
Tianhe (TH-2A)
54.9 Petaflops Peak

## Slide 19: Case Study
IBM Sequoia
IBM+ Lawrence Livermore National Laboratory
20.1 Petaflops Peak
16.32 Petaflops Sustain
1572864 IBM PowerPC cores
6MW of power !!
Huge amount of heat !!!

## Slide 20: Case Study
Google Data Center
Power: build data center close to power source (Sun, wind, etc.)
Cooling: sea water cooled data center

## Slide 21: Interconnects
Affects performance of both distributed and shared memory systems.
Two categories
  Shared memory interconnects
  Distributed memory interconnects

## Slide 22: Shared Memory Interconnects
Bus interconnect
  A collection of parallel communication wires together with some hardware that controls access to the bus.
  Communication wires are shared by the devices that are connected to it.
  As the number of devices connected to the bus increases, contention for use of the bus increases, and performance decreases.
Switched interconnect
  Uses switches to control the routing of data among the connected devices.

## Slide 23: Distributed Memory Interconnects
ring
toroidal mesh
Suppose p processors? How many links?

## Slide 24: Distributed Memory Interconnects
ring
toroidal mesh
Suppose p processors? How many links?
(3 – 1)*p/2 + 1*p = 2p
(5 – 1)*p/2 + 1*p = 3p
How to measure the “connectivity”

## Slide 25: Distributed Memory Interconnects
ring
toroidal mesh
Suppose p processors? How many links?
(3 – 1)*p/2 + 1*p = 2p
(5 – 1)*p/2 + 1*p = 3p
How to measure the “connectivity”

## Slide 26: Distributed Memory Interconnects
ring
toroidal mesh
Suppose p processors? How many links?
(3 – 1)*p/2 + 1*p = 2p
(5 – 1)*p/2 + 1*p = 3p
How to measure the “connectivity”
Bisection width:
The parallel system divided into 2 halves;
How many simultaneous communications can take Place “across the divide”between halves

## Slide 27: Distributed Memory Interconnects
ring
toroidal mesh
How to measure the “connectivity”
Bisection width:
The parallel system divided into 2 halves;
How many simultaneous communications can take Place “across the divide”between halves
2*p0.5

## Slide 28: Fully Connected Interconnects
Each switch is directly connected to every other switch.
impractical
Bisection width: p/2 * p/2
Links: (p-1)*p/2

## Slide 29: Hypercubes
one-
three-dimensional
two-
Dimension | Node | Bisection | Links
d |  |  | 

## Slide 30: Hypercubes
one-
three-dimensional
two-
Dimension | Node | Bisection | Links
d | 2d | p/2 | 1+d=1+log2(p)

## Slide 31: Crossbar Interconnects
Node | Switch | Bisection
P |  | 

## Slide 32: Crossbar Interconnects
Node | Switch | Bisection
P | P*P | P

## Slide 33: Omega Network
Node | Switch | Bisection
P |  | 

## Slide 34: Omega Network
Node | Switch | Bisection
P | 1/2*log2P*(2*2) | P

## Slide 35: Network Parameters
Any time data is transmitted, we’re interested in how long it will take for the data to finish transmission.
Latency
  The time that elapses between the source’s beginning to transmit the data and the destination’s starting to receive the first byte.
Bandwidth
  The rate at which the destination receives data after it has started to receive the first byte.

## Slide 36: Data Transmission Time
Message transmission time = l + n / b
latency (seconds)
bandwidth (bytes per second)
length of message (bytes)

## Slide 37: Memory Consistency Models
A memory consistency model gives the rules on when a write by one processor can be observed by a read on another, across different addresses.
  Strict Consistency: demand write operations are seen in order in which they were actually issued, which is essentially impossible to secure in distributed system as deciding global time is impossible.
  Sequential Consistency: every node of the system sees the write operations on the same memory part in the same order, although the order may be different from the real time issuing the operations.
  Casual Consistency: A system provides causal consistency if memory operations that potentially are causally related are seen by every node of the system in the same order.

## Slide 38: Memory Consistency Models
Release consistency
  Systems of this kind are characterized by the existence of two special synchronization operations, release and acquire.
  Before issuing a write to a memory object a node must acquire the object via a special operation, and later release it. Therefore the application that runs within the operation acquire and release constitutes the critical region.
  The system is said to provide release consistency, if all write operations by a certain node are seen by the other nodes after the former releases the object and before the latter acquire it.

## Slide 39: Cache Coherence
Programmers have no control over caches and when they get updated.
cache-1
A 2
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 2
memory
A 2->7

## Slide 40: Snooping Cache Coherence
Use snoopy mechanism to keep all processors’ view of memory coherent
M1
M2
M3
Snoopy
Cache
DMA
Physical
Memory
Memory
Bus
Snoopy
Cache
Snoopy
Cache
DISKS

## Slide 41: Snooping Cache Coherence
The cores share a bus .
Any signal transmitted on the bus can be “seen” by all cores connected to the bus.
When core 0 updates the copy of x stored in its cache it also broadcasts this information across the bus.
If core 1 is “snooping” the bus, it will see that x has been updated and it can mark its copy of x as invalid.

## Slide 42: Snooping Cache Protocols
M
S
I
M: Modified
S: Shared
I: Invalid
Each cache line has state bits
Address tag
state
bits
Write miss
(P1 gets line from memory)
Other processor
intent to write (P1 writes back)
Read miss
(P1 gets line from memory)
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Cache state in processor P1
Other processor reads
(P1 writes back)
MSI Protocol

## Slide 43: Example
M
S
I
Write miss
Read
miss
P1 intent to write
P2 intent to write
P2 reads,
P1 writes back
P1 reads
or writes
P2 intent to write
P1
M
S
I
Write miss
Read
miss
P2 intent to write
P1 intent to write
P1 reads,
P2 writes back
P2 reads
or writes
P1 intent to write
P2
P1 reads
P1 writes
P2 reads
P2 writes
P1 writes
P2 writes
P1 reads
P1 writes

## Slide 44: Memory Update
When a read-miss for A occurs in cache-2,
a read request for A is placed on the bus
  Cache-1 needs to supply & change its state to shared
  The memory may respond to the request also!
Cache-1 needs to intervene through memory controller to supply correct data to cache-2
cache-1
A 200
CPU-Memory bus
CPU-1
CPU-2
cache-2
memory (stale data)
A 100

## Slide 45: False Sharing
A cache block contains more than one word
Cache-coherence is done at the block-level and not word-level
Suppose M1 writes wordi and M2 writes wordk and
both words have the same block address.
What can happen?
state blk addr data0 data1 ... dataN

## Slide 46: Directory Cache Coherence
CPU
C$
Interconnection Network
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
CPU
C$
CPU
C$
CPU
C$
CPU
C$
CPU
C$
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
Data
Tag
Stat.
Each line in cache has state field plus tag
Data
Stat.
Directry
Each line in memory has state field plus bit vector directory with one bit per processor

## Slide 47: Cache States
For each cache line, there are 4 possible states
  C-invalid (= Nothing): The accessed data is not resident in the cache.
  C-shared (= Sh): The accessed data is resident in the cache, and possibly also cached at other sites. The data in memory is valid.
  C-modified (= Ex): The accessed data is exclusively resident in this cache, and has been modified. Memory does not have the most up-to-date data.
  C-transient (= Pending): The accessed data is in a transient state (for example, the site has just issued a protocol request, but has not received the corresponding protocol reply).

## Slide 48: Directory States
For each memory block, there are 4 possible states
  R(dir): The memory block is shared by the sites specified in dir (dir is a set of sites). The data in memory is valid in this state. If dir is empty (i.e., dir = ε), the memory block is not cached by any site.
  W(id): The memory block is exclusively cached at site id, and has been modified at that site. Memory does not have the most up-to-date data.
  TR(dir): The memory block is in a transient state waiting for the acknowledgements to the invalidation requests that the home site has issued.
  TW(id): The memory block is in a transient state waiting for a block exclusively cached at site id (i.e., in C-modified state) to make the memory block at the home site up-to-date.

## Slide 49: Protocol Message
Category | Messages
Cache to Memory Requests | ShReq, ExReq
Memory to Cache Requests | WbReq, InvReq, FlushReq
Cache to Memory Responses | WbRep(v), InvRep, FlushRep(v)
Memory to Cache Responses | ShRep(v), ExRep(v)
There are 10 different protocol messages

## Slide 50: Example
Write miss, to read shared line
Directory Controller
DRAM Bank
CPU
C$
1
Store request at head of CPU->Cache queue.
2
Store misses in cache.
3
Send ExReq message to directory.
4
ExReq message received at directory controller.
5
Access state and directory for line. Line’s state is R, with some set of sharers.
6
Send one InvReq message to each sharer.
11
ExRep arrives at cache
12
Update cache tag and data, then store data from CPU
Interconnection Network
CPU
Cache
7
InvReq arrives at cache.
8
Invalidate cache line. Send InvRep to directory.
9
InvRep received. Clear down sharer bit.
10
When no more sharers, send ExRep to cache.
Multiple sharers
CPU
Cache
CPU
C$