## Slide 1: CS427 Multicore Architecture and Parallel Computing
Lecture 2 Parallel Architecture
Li Jiang
2014/9/18

## Slide 2: Lecture Objectives
Understand the core concept, but not the detail
Refresh your memory on Computer architecture
The early path towards Parallelsim

## Slide 3: Basic Computer Model
input
output
programs
Computer runs one
program at a time.

## Slide 4: Discussion and debate
Who invented the computer?
  Von Neumann VS. Alan Turning

## Slide 5: The Von Neumann Machine
Fixed computer
  3-weeks to program on ENIAC
Stored-program computer
  Inst. Set in memory
  Self-modifying code

## Slide 6: Main Components
Main memory
  This is a collection of locations, each of which is capable of storing both instructions and data.
  Every location consists of an address, which is used to access the location, and the contents of the location.
CPU
  Control unit - responsible for deciding which instruction in a program should be executed.
  ALU - responsible for executing the actual instructions.
  Register – very fast storage, part of the CPU.
  Program counter – stores address of the next instruction to be executed.
Bus
  Wires and hardware that connects the CPU and memory.
Cache
  Fill the gap between CPU and main memory

## Slide 7: Pipeline
In this example:
  Sequential execution takes 4 * 90min = 6 hours
  Pipelined execution takes 30+4*40+20 = 3.5 hours
Bandwidth = loads/hour
BW = 4/6 l/h w/o pipelining
BW = 4/3.5 l/h w pipelining
BW <= 1.5 l/h w pipelining, more total loads
Pipelining helps bandwidth but not latency (90 min)
Potential speedup = Number pipe stages
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Dave Patterson’s Laundry example: 4 people doing laundry
wash (30 min) + dry (40 min) + fold (20 min) = 90 min Latency

## Slide 8: Pipeline

## Slide 9: Multiple Issue
Multiple issue processors replicate functional units and try to simultaneously execute different instructions in a program.
adder #1
adder #2
z[1]
z[3]
z[2]
z[4]
for (i = 0; i < 1000; i++)
z[i] = x[i] + y[i];

## Slide 10: Multiple Issue
Static multiple issue
  functional units are scheduled at compile time.
Dynamic multiple issue
  functional units are scheduled at run-time.
  Allow instruction behind stalls to proceed
  Enable out-of-order execution and out-of-order completion
  Tomasulo algorithm
.

## Slide 11: Register Renaming
Multiple issue challenge
  WAR, WAW harzard
  Limited register resource
  Register renaming

## Slide 12: Loop Unrolling
for (i = 1 to bignumber)
A(i)
B(i)
C(i)
end
  Without Unrolling: A(1) X X B(1) X X C(1) X X ...

## Slide 13: Loop Unrolling
for (i = 1 to bignumber)
A(i)
B(i)
C(i)
end
After Unrolling:
for (i = 1 to bignumber/3)
A(i)
A(i+1)
A(i+2)
B(i)
B(i+1)
B(i+2)
C(i)
C(i+1)
C(i+2)
end
  Without Unrolling: A(1) X X B(1) X X C(1) X X ...
  With Unrolling: A(1) A(2) A(3) B(1) B(2) B(3) C(1) C(2) C(3) ...

## Slide 14: Software Pipelining
for (i = 1 to bignumber)
A(i) ; 3
B(i) ; 3
C(i) ; 12(perhaps a floating point operation)
D(i) ; 3
E(i) ; 3
F(i) ; 3
End
Software Pipelining:
for i = (1 to bignumber - 6)
A(i+6)
B(i+5)
C(i+4)
D(i+2)
E(i+1)
F(i)
end

## Slide 15: Software Pipelining
for (i = 1 to bignumber)
A(i) ; 3
B(i) ; 3
C(i) ; 12(perhaps a floating point operation)
D(i) ; 3
E(i) ; 3
F(i) ; 3
End
Software Pipelining:
for i = (1 to bignumber - 6)
A(i+6)
B(i+5)
C(i+4)
D(i+2)
E(i+1)
F(i)
end
Iteration 1: A(7) B(6) C(5) D(3) E(2) F(1)
Iteration 2: A(8) B(7) C(6) D(4) E(3) F(2)
Iteration 3: A(9) B(8) C(7) D(5) E(4) F(3)
Iteration 4: A(10) B(9) C(8) D(6) E(5) F(4)
Iteration 5: A(11) B(10) C(9) D(7) E(6) F(5)
Iteration 6: A(12) B(11) C(10) D(8) E(7) F(6)
Iteration 7: A(13) B(12) C(11) D(9) E(8) F(7)

## Slide 16: Speculation
In speculation, the compiler or the processor makes a guess about an instruction, and then executes the instruction on the basis of the guess
Always speculate the branch is taken, 1/1000 error rate!
for (i = 0; i < 1000; i++)
z[i] = x[i] + y[i];

## Slide 17: Speculation
for (i = 0; i < 1000; i++)
z[i] = x[i] + y[i];

## Slide 18: ILP in a Realistic Machine

## Slide 19: Vector Processing
+
Scalar processing
  traditional mode
  one operation produces one result
SIMD processing
  with SSE / SSE2
  one operation produces multiple results
  Limitation (branch divergence)
X
Y
X + Y
+
x3
x2
x1
x0
y3
y2
y1
y0
x3+y3
x2+y2
x1+y1
x0+y0
X
Y
X + Y
Slide Source: Alex Klimovitski & Dean Macri, Intel Corporation

## Slide 20: Vector Processing
Year
16x bytes
4x floats
2x doubles
Intel SSE2 data types: anything that fits into 16 bytes
Instructions perform add, multiply etc. on all the data in this 16-byte register in parallel
Pros:
  Saving decode time, execute I automaticallyexecute I+1 …
Challenges:
  Need to be contiguous in memory and aligned, addressing
  Some instructions to move data around from one part of register to another

## Slide 21: Vector Processing
Vector Register
  Fixed length bank holding a single vector has at least 2 read and 1 write ports typically 8-32 vector registers, each holding 64-128 64-bit elements
Vector Functional Units (FUs)
  Fully pipelined, start new operation every clock typically 4 to 8 FUs: FP add, FP mult, FP reciprocal (1/X), integer add, logical, shift; may have multiple of same unit
Vector Load-Store Units (LSUs)
  fully pipelined unit to load or store a vector; may have multiple LSUs
Scalar registers
  Single element for FP scalar or address
Cross-bar to connect FUs , LSUs, registers

## Slide 22: Vector Processing
Interleaved memory
  Multiple “banks” of memory
  Access independently

## Slide 23: Vector Processing
Interleaved memory
  Multiple “banks” of memory
  Access independently
  How to distribute the data of a vector?

## Slide 24: Vector Processing
Interleaved memory
  Multiple “banks” of memory
  Access independently
  How to distribute the data of a vector?
  Elements of a vector are distributed across multiple banks

## Slide 25: Vector Processing
Interleaved memory
  Multiple “banks” of memory
  Access independently
  Elements of a vector are distributed across multiple banks
Strided memory access and hardware scatter/gather
  Access element of a vector located at fixed/iregular intervals
add | data
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
Hardware accelerator
WHY？

## Slide 26: Vector Processing
Year
How it works
  Suppose there are n * n data to be processed
  But the width of vector processor is m, m < n
for ( i = 0 ; i < n; i++)
for ( j = 0; j < n; j++){
A[i][j] = -A[i][j]
}

## Slide 27: Vector Processing
Year
How it works
  Suppose there are n * n data to be processed
  But the width of vector processor is m, m < n
  Divide problem into blocks, execute block by block
for ( i = 0 ; i < n; i++)
for ( j = 0; j < n; j++){
A[i][j] = -A[i][j]
}

## Slide 28: Vector Processing
Year
Branch divergence
  Single instruction requires all the ALUs execute the same instruction or are idle
  Degrade the overall performance
for ( i = 0 ; i < n; i++)
for ( j = 0; j < n; j++){
if (A[i][j] < 0)
A[i][j] = -A[i][j]
}

## Slide 29: Vector Processing
Year
Branch divergence
  Single instruction requires all the ALUs execute the same instruction or are idle
  Degrade the overall performance
for ( i = 0 ; i < n; i++)
for ( j = 0; j < n; j++){
if (A[i][j] < 0)
A[i][j] = -A[i][j];
else
A[i][j] = 2*A[i][j];
}

## Slide 30: Vector Processing
Year
Vector-mask control takes a Boolean vector
  when vector-mask registers loaded from vector test, vector instructions operate only on vector elements whose corresponding entries in the vector-mask register are 1.
  Still requires clock even if result not stored
if (A[i][j] < 0)
A[i][j] = -A[i][j]
M[i][j] = (A[i][j] < 0)
A[i][j] -= M[i][j]*2*A[i][j]

## Slide 31: “DLXV” Vector Instructions
Instr. Operands Operation Comment
ADDV V1,V2,V3 V1=V2+V3 vector + vector
ADDSV V1,F0,V2 V1=F0+V2 scalar + vector
MULTV V1,V2,V3 V1=V2xV3 vector x vector
MULSV V1,F0,V2 V1=F0xV2 scalar x vector
LV V1,R1 V1=M[R1..R1+63] load, stride=1
LVWS V1,R1,R2 V1=M[R1..R1+63*R2] load, stride=R2
LVI V1,R1,V2 V1=M[R1+V2i,i=0..63] indir.("gather")
CeqV VM,V1,V2 VMASKi = (V1i=V2i)? comp. setmask
MOV VLR,R1 Vec. Len. Reg. = R1 set vector length
MOV VM,R1 Vec. Mask = R1 set vector mask

## Slide 32: Vector Processing
Easy to get high performance
  N operations:
  are independent
  use same functional unit
  access disjoint registers
  access registers in same order as previous instructions
  access contiguous memory words or known pattern
  can exploit large memory bandwidth
  hide memory latency (and any other latency)
Scalable
  get higher performance as more HW resources available
Compact
  Describe N operations with 1 short instruction (v. VLIW)
Predictable
  (real-time) performance vs. statistical performance (cache)
Multimedia ready
  choose N * 64b, 2N * 32b, 4N * 16b, 8N * 8b

## Slide 33: Multithreading
Hardware multithreading provides a means for systems to continue doing useful work when the task being currently executed has stalled.
  No dependency between inst. From different threads
  Ex., the current task has to wait for data to be loaded from memory
Coarse-grained - only switches threads that are stalled waiting for a time (e.g., L2 cache miss)-consuming operation to complete.
  Pros: switching threads doesn’t need to be nearly instantaneous.
  Cons: the processor can be idled on shorter stalls, and thread switching will also cause delays.
  Share CPU/RF/Cache, fast context switching
Fine-grained - the processor switches between threads after each instruction, skipping threads that are stalled.
  Pros: potential to avoid wasted machine time due to stalls.
  Cons: a thread that’s ready to execute a long sequence of instructions may have to wait to execute every instruction.
  More redundancy
Excute

## Slide 34: Multithreading
Simultaneous Multithreading (SMT)
Ins. from different threads

## Slide 35: Parallel Processors

## Slide 36: Memory Hierarchy
Most programs have a high degree of locality in their accesses
  spatial locality: accessing things nearby previous accesses
  temporal locality: reusing an item that was previously accessed
Memory hierarchy tries to exploit locality
on-chip cache
registers
datapath
control
processor
Second level cache (SRAM)
Main memory
(DRAM)
Secondary storage (Disk)
Tertiary storage
(Disk/Tape)
Speed | 1ns | 10ns | 100ns | 10ms | 10sec
Size | B | KB | MB | GB | TB

## Slide 37: Memory Hierarchy
Intel i7

## Slide 38: Processor-DRAM Gap
µProc
60%/yr.
DRAM
7%/yr.
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
Time
“Moore’s Law”
Memory hierarchies are getting deeper
  Processors get faster more quickly than memory

## Slide 39: News: 3D Memory Cube
Micron

## Slide 40: News: 3D Memory Cube

## Slide 41: Cache Mappings
Full associative
  a new line can be placed at any location in the cache.
Direct mapped
  each cache line has a unique location in the cache to which it will be assigned.
n-way set associative
  each cache line can be place in one of n different locations in the cache.

## Slide 42: Cache Write
Cache write
  the value in cache may be inconsistent with the value in main memory.
Write-through caches
  handle this by updating the data in main memory at the time it is written to cache.
Write-back caches
  mark data in the cache as dirty. When the cache line is replaced by a new cache line from memory, the dirty line is written to memory.

## Slide 43: Reduce Misses
Classifying Misses: 3 Cs
Compulsory
  The first access to a block is not in the cache, so the block must be brought into the cache. Also called cold start missesor first reference misses.(Misses in even an Infinite Cache)
Capacity
  If the cache cannot contain all the blocks needed during execution of a program, capacity misses will occur due to blocks being discarded and later retrieved.(Misses in Fully Associative Size X Cache)
Conflict
  If block-placement strategy is set associative or direct mapped, conflict misses (in addition to compulsory & capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. Also called collision missesor interference misses.(Misses in N-way Associative, Size X Cache)
Maybe four: 4th “C”
  Coherence-Misses caused by cache coherence: data may have been invalidated by another processor or I/O device

## Slide 44: Cache and Program
Assuming only two cache lines
Indirect control the cache
  Cache are controlled by hardware
  Programmer don’t directly determine which data and which instructions are in the cache
  Knowing the principle of spatial and temporal locality allows us to have indirect control

## Slide 45: Cache and Program

## Slide 46: Common Techniques
Merging Arrays
  improve spatial locality by single array of compound elements vs. 2 arrays
Permuting a multidimensional array
  improve spatial locality by matching array layout to traversal order

## Slide 47: Common Techniques
Merging Arrays
  improve spatial locality by single array of compound elements vs. 2 arrays
Permuting a multidimensional array
  improve spatial locality by matching array layout to traversal order

## Slide 48: Common Techniques
Merging Arrays
  improve spatial locality by single array of compound elements vs. 2 arrays
Permuting a multidimensional array
  improve spatial locality by matching array layout to traversal order
Loop Interchange
  change nesting of loops to access data in order stored in memory
Loop Fusion
  Combine 2 independent loops that have same looping and some variables overlap
Blocking
  Improve temporal locality by accessing “blocks” of data repeatedly vs. going down whole columns or rows
  Matrix Multiplication

## Slide 49: Second Level Cache
L2 Equations
  AMAT = Hit TimeL1+ Miss RateL1x Miss PenaltyL1
  Miss PenaltyL1= Hit TimeL2+ Miss RateL2x Miss PenaltyL2
  AMAT = Hit TimeL1+Miss RateL1x (Hit TimeL2+Miss RateL2+ Miss PenaltyL2)
  Local miss rate—misses in this cache divided by the total number of memory accesses to this cache(Miss rateL2)
  Global miss rate—misses in this cache divided by the total number of memory accesses generated by the CPU(Miss RateL1x Miss RateL2)
  Global Miss Rate is what matters

## Slide 50: Virtual Memory
If we run a very large program or a program that accesses very large data sets, all of the instructions and data may not fit into main memory.
Virtual memory functions as a cache for secondary storage.
It only keeps the active parts of running programs in main memory.
Swap space
  those parts that are idle are kept in a block of secondary storage.
Pages
  blocks of data and instructions. Usually these are relatively large. Most systems have a fixed page size that currently ranges from 4 to 16 kilobytes.

## Slide 51: Virtual Memory
Program with 4 pages (A, B, C, D)
Any chunk of Virtual Memory assigned to any chuck of Physical Memory (“page”)
Physical Memory
Virtual Memory
A
B
C
D
D
A
B
C
0
4 KB
8 KB
12 KB
0
4 KB
8 KB
12 KB
16 KB
20 KB
24 KB
28 KB
Disk
Use the physical address in virtual memory?
In a multitasking OS, if multiple programs access to the same address
How we design address?

## Slide 52: Address Mapping

## Slide 53: Page Fault

## Slide 54: Main Memory
Performance of Main Memory
  Latency: Cache Miss Penalty
  Access Time: time between request and word arrives
  Cycle Time: time between requests
  Turn around time (write-read)
  Burst read/write mode
  Bandwidth: I/O & Large Block Miss Penalty (L2)
Main Memory is DRAM: Dynamic Random Access Memory
  Dynamic since needs to be refreshed periodically (8 ms, 1% time)
  Addresses divided into 2 halves (Memory as a 2D matrix):RAS or Row Access Strobe
  CAS or Column Access Strobe
Cache uses SRAM: Static Random Access Memory
  No refresh (6 transistors/bit vs. 1 transistor)
  Size: DRAM/SRAM 4-8,
  Cost/Cycle time: SRAM/DRAM 8-16

## Slide 55: Memory Organization

## Slide 56: Main Memory Performance

## Slide 57: Avoid Bank Conflict
Even a lot of banks, still bank conflict in certain regular accesses
e.g. Storing 256x512 array in 512 banks and column processing (512 is an even multiple of 128)
0,0 0,1 ,..., 0,127 ,..., 0,511
1,0 1,1 ,..., 1,127 ,..., 1,511
...
127,0 127,1 ,..., 127,127 ,..., 127,511
...
128,0 128,1 ,..., 128,127 ,..., 128,511
...
255,0 255,1 ,..., 255,127 ,..., 255,511
Bank0 Bank1 Bank127 ,…, Bank511
int x[256][512];
for (j = 0; j < 512; j = j+1)
for (i = 0; i < 256; i = i+1)
x[i][j] = 2 * x[i][j];
Column processing
Column elements are in the same bank
Inner Loop is a column processing which causes bank conflicts